## Slide 1: Job-shop Scheduling
n jobs m machines
No recirculation
  Jobs do not revisit the same machine
(i, j) is referred to as an operation in which job j is processed on machine i
Processing time is pij
Objective is to minimize Cmax – makespan – max completion time
Jobs have a machine sequence
Find the sequence for each machine

## Slide 2: Training matrix analogous to Job shop Scheduling
There are n trainees (jobs)
There are m departments (machines)
Each trainee has a pre-determined sequence based on their qualification
Each trainee spends a different number of weeks in each department based on their final placements.
Find a schedule that minimizes the completion time of all required training for this new batch of trainees.

## Slide 3: Hospital sequencing
Medical depts have equipment and doctors which are like the machines
Jobs are patients, who are scheduled to arrive the next day.
Each patient has a pre-determined sequence for testing and consultation based on their ailment
Each patient spends a different amount of time in each medical department (with equipment, doctors) based on their ailment.
Find a schedule that minimizes the completion time for all patient diagnostics and doctor consultations.

## Slide 4: Job-shop Scheduling 4 m/c and 3 jobs
Jobs j m/c i seq pij
1 1 2 3 p11=10, p21=8, p31=4
2 2 1 4 3 p22 = 8, p12=3, p42=5, p32=6
3 1 2 4 p13=4, p23=7, p43=3

## Slide 5: Job-shop Scheduling
Conjunctive (solid arcs) and disjunctive (dotted arcs)
Conjunctive – machine sequence for a job
Disjunctive – job sequence for a machine
1 sink because the completion time of the last job is important to obtain minimum makespan ‘Cmax’ to complete all jobs
1,1
2,1
3,1
U
2,2
1,2
4,2
3,2
V
1,3
2,3
4,3
Sink
Source
P23 =7
0
4
3
4
6
5
3
8
8
10
0
0

## Slide 6: Job-shop Scheduling
IP solution
Let yij be starting time of job j on machine i
Minimize Cmax
s.t.
ykj – yij >= pij for all (i,j) (k,j) (for the job)
Cmax - yij >= pij for all (i,j) (for the job)
yij-yil >= pil or yil –yij >= pij for all (i,l) and (i,j) i = 1……m (for the machine)
yij >= 0
Solve using branch and bound
  Computationally prohibitive for large n and m (see page 72 and 74 of text)

## Slide 7: Shifting Bottleneck Heuristic
Very efficient heuristic for n job m machine job shop with jobs having a pre-determined sequence
Has been proven to be very close to optimal, which has been verified numerous times with the branch and bound optimal search.
Proven to be very fast compared to B&B

## Slide 8: Shifting Bottleneck Heuristic – completion time
M is the set of all machines
Mo is the set of machines for which the sequence has been determined
An iteration results in selecting a machine from M-Mo for inclusion in Mo.
  Each machine in M-Mo is considered as a single machine problem with release and due dates for which the maximum lateness is to be minimized (Lmax)
  Then the machine with the largest Lmax is chosen and is termed as a bottleneck. This is included in Mo
  Update Cmax = Cmax + Lmax
  Re-sequence all machines in Mo-the last machine added.
  Continue until M-Mo is a null set.
Release date of job j on machine i is the longest path from source to node (i,j)
Due date of job j on machine i is the longest path from node (i,j) to sink – pij and the resultant is subtracted from Cmax of set Mo

## Slide 9: Shifting Bottleneck Heuristic
Gantt Chart
M1
M2
M3
M2
M1
M4
M3
M1
M2
M4
J1
J2
J3
10 18 22
8 11 16 22
4 11 14
M1
M2
M3
M4
J1
J2
J3
J2
J1
J3
10 13 17
8 10 18 24
J2
J1
18 22 28
J2
J3
13 18 25 28
See handout for solution
Slack 1
Slack 4

## Slide 10: Composite Dispatching rules
ATC Apparent tardiness cost
ATCS Apparent tardiness cost with set up
    See page 446

## Slide 11: Shifting Bottleneck Heuristic – weighted tardiness
M is the set of all machines
Mo is the set of machines for which the sequence has been determined
An iteration results in selecting a machine from M-Mo for inclusion in Mo.
  Each machine in M-Mo is considered as a single machine problem with release and due dates for which a priority index is calculated Iij(t)
  Iij(t) is computed using the ATC rule (Apparent Tardiness Cost)
  Sequence jobs on the machine with the highest to lowest Iij(t)
  Calculate weighted tardiness
  Then the machine with the largest weighted tardiness is chosen and is termed as a bottleneck. This is included in Mo
  Re-sequence all machines in Mo-the last machine added.
  Continue until M-Mo is a null set.
Release date of job j on machine i is the longest path from source to node (i,j)
Due date of job j on machine i is the longest path from node (i,j) to sink – pij and the resultant is subtracted from Cmax of set Mo
  If a path does not exist then make it infinity.

## Slide 12
Jobs wj rj dj m/c seq pij
1 1 5 24 1 2 3 p11=5, p21=10, p31=4
2 2 0 18 3 1 2 p32 = 4, p12=5, p22=6
3 2 0 16 3 2 1 p33=5, p23=3, p13=7
Shifting Bottleneck Heuristic – weighted tardiness

## Slide 13: Shifting Bottleneck Heuristic – weighted tardiness
3 sinks because the completion time of all jobs is important
1,1
2,1
3,1
U
3,2
1,2
2,2
V
3,3
2,3
1,3
Sink
Source
P23 =3
0
5
7
4
6
5
4
10
5
0
5
V
V
Sink
Sink
See handout for solution

## Slide 14: Shifting Bottleneck Heuristic – weighted tardiness
ATC Rule:
  t is the earliest time at which machine i can be used
  K is a scaling parameter
  is the average processing time for machine i
Weighted Tardiness
  Ck’ is the completion time of job k at the beginning of an iteration
      Ck” is the new completion time of job k at the end of an iteration

## Slide 15: Software for Job shop scheduling
LEKIN
Summary
  Single machine scheduling
    With or without setup time
  Parallel machines (machines can process all jobs)
  Flow shop (All jobs have to flow first on one machine and then on another)
  Job-shop
    Minimize Completion time
    Minimize Weighted Tardiness
  Flexible flow shop
Methods
  Dispatching rules, Tabu, Simulated Annealing, Shifting bottleneck heuristics for completion time and weighted tardiness objective.