## Slide 1: Flexible Assembly line
Minimum part set (MPS)
Suppose there are l product types. Let Nl denote the number of jobs for each product type l. If z is the greatest common divisor (GCD) of integers N1 …Nl then the vector
(N1/z,…..Nl/z)
is the smallest set having the same proportions of different product types. This set is called the minimum part set. It is used to determine the cyclic schedule and the cycle time for the schedule.
Cycle time is determined after steady state conditions have been reached.
See chapter 6

## Slide 2: 3 Heuristics
Unpaced flexible assembly line
  Profile fitting heuristic (PF)
Paced flexible assembly line
  Grouping and Spacing Heuristic
Flexible Flow systems with Bypass
  Flexible flow line loading algorithm is used (FFLL)

## Slide 3: Unpaced Flexible Assembly line
Consider a number of machines in series with a limited buffer between them
The material handling system that move the product from one to the next machine is unpaced
Bypass is not allowed
A machine can release its product to the next only if there is space in the buffer otherwise it is blocked
Machines serve jobs in a first-in-first-out FIFO system.
Goal: find min cycle time or same as saying max throughput
Ex: Assembly of televisions or copiers
The buffer space is viewed as a machine with no processing time.
  So a system with buffers is transformed into a system with no buffers, which make it easy to solve.

## Slide 4: Unpaced Flexible Assembly line
Profile fitting heuristics
Select a job with the largest total processing time as the first job in the MPS
For all the remaining jobs, consider each one of them- one at a time - and schedule it as the next job
Calculate the total nonproductive time on all the machines
Select the job with the lowest total nonproductive time as the next job in the partial sequence
Stop when all the jobs in the MPS have been scheduled
Weighted Profile fitting heuristics
  A weight is given to the nonproductive time on each machine

## Slide 5: Unpaced Flexible Assembly line
Jobs 1 2 3 4
P1j 2 4 2 3
P2j 4 4 0 2
P3j 2 0 2 0
Weights on nonproductive time
machine 1 and 2 = 2
Machine 3 = 1

## Slide 6: Paced Flexible Assembly line
Paced lines have a conveyor to move the jobs.
  Examples car assembly line
Jobs maintain a fixed distance from one another.
Cycle time is the reciprocal of production rate
Stations are different segments of the assembly line
Sometimes the workers walk along with the job as the conveyor moves.
Bypass is not allowed
Grouping and Spacing Heuristic (GS)
Goal: multiple objectives: minimize total cost (set-up cost, spacing cost, tardiness cost
See chapter 6, page 126-127 for goals and steps of the heuristic.

## Slide 7: Scheduling of Flexible Flow systems with Bypass
Ex. Printed Circuit Boards
Assembly line with several stages. Some of the stages have parallel machines
In a stage, a job is a batch of identical items has to be processed only on any one machine if the stage has parallel machines
Bypassing stages is allowed
Limited buffer size at a stage.
  If buffer is full, then the material handling stops or the jobs must bypass the stage and recirculate.
Obj function: Maximize throughput or minimizing the cycle time of the MPS and reduce Work-in process (WIP)
Flexible flow line loading algorithm is used (FFLL)

## Slide 8: Scheduling of Flexible Flow systems with Bypass
FFLL has 3 phases
The machine allocation phase
  Obtain nearly balanced workload by using the longest processing time first (LPT) rule
The sequencing phase
  Determines the order in which jobs are sequenced on the machines
  Uses a dynamic balancing heuristic
  Define workload in a MPS for machine i is
  Total workload W =
  Let overload at machine i due to job j entering the system be defined as oij = pij – (pj Wi /W)
  oij is negative indicates underload
  Cumulative Overload Oij = Sj jobs that are sequenced including j
  Obj func is minimize

## Slide 9: Scheduling of Flexible Flow systems with Bypass
The release timing phase: Reduce work-on-process (wait times)
The machine with the greatest MPS workload is the bottleneck, since MPS cycle time cannot be smaller than the workload of the bottleneck machine.
  Consider one machine at a time and schedule jobs based on the sequence as and when they are available.
  Delay jobs as much as possible that are upstream to the bottleneck machine without altering the sequence.
    Delays are calculated based on the starting point of the jobs on the bottleneck machine
  Process all jobs as soon as possible on the machines that are downstream to the bottleneck machine
See chapter 6