## Slide 1: On Detection and Concealment of Critical Roles in Tactical Wireless Networks
Zhuo Lu
University of Memphis
Cliff Wang
Army Research Office
Mingkui Wei
NC State University

## Slide 2
Introduction
System Models
Role Detection
Role Concealment
Conclusion

## Slide 3: Introduction
Tactical wireless networks:
  Mission-critical mobile ad-hoc networks.
  Allows two-way communication for warfighters.
  Unique challenges due to tactical requirements, e.g., reliability and security in hostile environment.

## Slide 4: Introduction
Characters of tactical wireless network:
  Nodes in the network are not homogenous.
  Commanding and control nodes lead to a one-to-multiple communication model.

## Slide 5: Research Question
How to detect and conceal the roles of nodes in tactical wireless networks?
  Roles of nodes:
    Commanding role: # of active network flow with other nodes exceeds a given threshold (not necessarily real commanders).
    Acting role: otherwise.
  Two-fold questions:
    Whether we can accurately identify commanding nodes in a network from an adversary’s point of view.
    Whether we can protect such nodes from being identified from a defender’s point of view.

## Slide 6: Contributions
  Provide an initial study on role detection and concealment, which are important in tactical wireless networks.
  Propose role detection and concealment methods and comprehensively evaluate their performance.

## Slide 7
Introduction
System Models
Role Detection
Role Concealment
Conclusion

## Slide 8: Network Model
Network Model
  Consider a network with n nodes distributed on region independently and uniformly.
  Node density λ is large enough such that the network is connected.
  Two nodes are connected if within each other’s transmission range r.

## Slide 9: Roles of Nodes
Commanding and Acting roles:
  A node is commanding if it has network flows with rates in rate region Σ to/from at least nodes.
    For example, , .
  A node is acting otherwise.
  Mathematically representation:
    A role vector contains roles of all nodes.

## Slide 10: Adversary Model
Goal of attackers
  To successfully detect the role of each node, i.e., , within a sufficiently long time period.
Capability of attackers
  Can overhear the data transmissions on each link.
  Can estimate the transmission rate at each link.
  Is aware of the network topology and knows the routing path between any source-destination pair.

## Slide 11: Problem Statement
Role detection
  The goal of the attacker is to find an estimate which is close to the real role vector .
  In the best case, should be minimized.
Role concealment
  The goal of the defender is to make difficult be estimated.
  In the best case, the probability that should be 0.5, i.e., a random 0/1 guess.

## Slide 12
Introduction
System Models
Role Detection
Role Concealment
Conclusion

## Slide 13: Role Detection
Network tomography
  A network with nodes has at most undirected flows.
  Estimate the real flow vector , from the observed link rate vector , where is the p2p links in the network).
  Linear relationship exist between and :
  ,
  where is 1 if -th link is on the routing path of flow .

## Slide 14: Detection Approach
Flow rate estimation
  Make estimation to be close to the real value .
Role detection
  Estimate role of node ,
    ,
    where is the rate threshold range, is the threshold for role detection.

## Slide 15: Evaluation
Simulation setup
  100-nodes network with density 5;
  Transmission range is normalized to 1;
  2 commanding nodes and 98 acting nodes;
  Commanding nodes communicates to 10 other nodes.
  10 random acting to acting communication pairs.
  Rate of each flow is random between 1M and 2M bps.

## Slide 16: Evaluation
Result of flow rate estimation
  Most of flow rates can be accurately estimated.
  Proper thresholds can help in role detection.

## Slide 17: Evaluation
Result of role detection
  , and .
  Metrics:
    Flow detection error rate.
    Commanding role detection rate.
    Commanding role false alarm.
    Overall role detection error rate.

## Slide 18: Evaluation
Impact of threshold
  Keep , and change from 3 to 7.
  provides good performance (can be application specific as well).

## Slide 19
Introduction
System Models
Role Detection
Role Concealment
Conclusion

## Slide 20: Role Concealment
Flow detection and countermeasure
  a: normal network operation.
  b: deception traffic.
  c: changing routing strategies.

## Slide 21: Evaluation
Deception traffic
  Commanding role detection ratio ≈ 75%.
  Commanding role false alarm rise to 43.5%.
  Effective in conceal commanding roles.

## Slide 22: Evaluation
Routing changing
  Use k-th shortest path, instead of the shortest path for routing.
  Commanding role detection ratio ≈ 50%.
  Delay degradation is notecible.

## Slide 23
Introduction
System Models
Role Detection
Role Concealment
Conclusion

## Slide 24: Conclusion
Role detection in tactical wireless networks
  It is possible to identify critical role of nodes accurately.
Role concealment in tactical wireless networks
  Deception traffic.
  Routing changing.
  Both can effectively conceal critical role of nodes with compromise in network performance.

## Slide 25
Thank you!