Instructions

Read the emergency situation. Study the diagram until you understand the location of the workers and equipment in the situation. Do them one at a time. Don’t jump ahead, but you may look back to earlier questions and answers.

Background

You are acting section foreman during the absence of the regular section foreman.

You are at the face of the #5 entry on the 001 section making pre-shift checks for the oncoming second shift.

Miners from the first shift are working on the two other active sections in this mine.

Section 001 is 3,500 feet from the portal.

This mine has an average seam height of 36 inches.

The mine is dry, dusty, and not well rock dusted.

The section EMT, Claude Kildare, is the scoop operator. At the moment you think he is at the supply hole unloading bolts and plates.

You are well trained in basic first aid procedures.

A water line, with fire hose outlets and fire hose, extends the full length of the belt.

A one inch flexible water line runs from the dumping point to the continuous miner.

Including yourself, there are 12 miners working on this section today.

Rubber tired battery operated scoops are used to transport supplies and miners to the section.

Problem

As you complete your pre-shift checks of the face area of the #5 entry, you hear someone yelling "Fire!" You crawl out from the face of #5 entry into the last open crosscut and turn right toward the #3 entry. You see the continuous miner burning in the crosscut between #2 and #3 entries.

Study the map.

Question 1

You find the continuous miner engulfed in dense black smoke and large orange flames. The fire suppression system on the mining machine is not working. The fire is spreading rapidly, fed by oil and loose coal dust that have accumulated on the machine. Billy Bob, the miner operator is lying on his right side on the mine bottom about 15 feet in front of the miner on the fresh air side of the fire. Rambo, a buggy operator, and Joe are bent over him. Rambo says, "Billy Bob is hurt bad!"

What should you do now? (Select as MANY as you think are correct.)

- Before you do anything else, go to Billy Bob and begin first aid.

- Send Joe to the power box to de-energize the continuous miner and to bring back a couple of fire extinguishers.

- Tell Rambo and Joe to put on their filter self rescuers and you do the same.

- Put on your filter self-rescuer and then manually activate the fire suppression valve on the miner.

- Look at the mine roof over Billy Bob and the miner to see if it is O.K.

- Send Rambo across the section in fresh air to get Claude, the EMT, and to warn other miners and have them assemble at the dinner hole.

- Put Billy Bob on a piece of brattice curtain and have Rambo and Joe drag him to the dinner hole immediately so Claude can begin first aid treatment.

When you have made your selection(s) complete the next question.

Question 2

Joe has gone to knock the power to the miner, and Rambo is warning other miners and getting Claude to help you take care of Billy Bob. You start checking Billy Bob’s injuries. The left side of his face is covered with blisters. He is dazed and doesn’t recognize you. He is moaning softly. The skin on both his hands and fingers is charred. His coveralls are singed.

What should you do now? (Select as MANY as you think are correct.)

- Check his airway and breathing while taking his pulse on the unburned side of his neck.

- Ask him what happened and to tell you where he is hurt.

- Begin treating the burns on his face and hands by wrapping them gently with the clean inside part of you shirt or jacket.

- Shine your cap lamp into his eyes, one at a time, and look at his pupils.

- Feel his skull and spine with your fingertips.

- Quickly check him for other injuries.

- Ask him to wiggle the toes of his boots.

When you have made your selection(s) complete the next question.

Question 3

Your survey of Billy Bob’s injuries has taken about a minute. Based upon what you have found, what is wrong with him?

(Select as MANY as you think are correct.)

- First degree burns to the hands and face.

- Second degree burns to the hands and fingers.

- Third degree burns to the hands and fingers.

- Second degree burns to the face.

- Possible head or spinal injury.

- Shock.

- Heat exhaustion.

- Possible injury to his airway and lungs from smoke inhalation.

When you have made your selection(s) complete the next question.

Question 4

Claude arrives on the scene with the first aid kit. You tell him what you have found. He begins to treat Billy Bob and confirms your assessment. You notice the roof over the miner is working and some small pieces of shale are failing in front on the miner, near Billy Bob, Claude, and you.

What should you do now? (Select ONLY one.)

- Go get a couple of roof jacks and set them around Billy Bob and Claude.

- Help Claude stabilize Billy Bob so you can move him to a safer place as soon as possible.

- Continue to watch the roof carefully. If it gets worse, tell Claude to help you move Billy Bob to a safer spot.

- Immediately tell Claude to help you use a clothing drag to move Billy Bob to a safer place.

- Help Claude carefully roll Billy Bob onto the stretcher. Then secure him to the stretcher, cover him with a blanket and take him to the dinner hole.

When you have made your selection(s) complete the next question.

Question 5

You and Claude move Billy Bob to #4 entry in the last open cross cut. Claude is taking care of Billy Bob. Rambo and Joe come back with two small fire extinguishers and say they told everybody they saw to meet at the dinner hole. The whole continuous miner is now nearly covered with smoke and flames.

What should you do now? (Select as MANY as you think are correct.)

- Continue to help take care of Billy Bob.

- Tell Rambo and Joe to go behind the miner, cur the water line, and attack the fire.

- Tell Rambo and Joe to attack the fire from the fresh air side with the two fire extinguishers.

- After Billy Bob has been placed on the stretcher and stabilized, tell Claude and Joe to move him to the dinner hole.

- Send Rambo to the feeder in the belt entry to hook up a hose line and bring it to the fire while staying in fresh air.

- Go to the assembly point and make a head count.

- Call the surface. Report the conditions on the section and ask for help.

When you have made your selection(s) complete the next question.