# Symbol					Description					 Value and/or Units

| a |  | 1.570, dimensionless |
| --- | --- | --- |
| b |  | 1.570, dimensionless |
| (T/(t | cooling rate | (C/hour |
| (TLiquid/(t | cooling rate of the magma | (C/hour |
| erf(() | error function | -- |
| G | crystal growth rate | cm/sec |
| G’ | intercept for log(G) vs. log((T/(t) relation given by Cashman (1993) | cm/sec |
| I | nucleation rate | number/cm3/sec |
| I’ | intercept for log(I) vs. log((T/(t) relation given by Cashman (1993) | number/cm3/sec |
| inverf(() | inverse error function | -- |
| K1 | thermal conductivity of the country rock and solidified magma | 10260.0 J/m.hr.(C |
| K2 | thermal conductivity of the magma | 10260.0 J/m.hr.(C |
| L | crystal size | cm |
| m | exponent for the nucleation rate vs. cooling rate relation given by Cashman (1993) | dimensionless |
| n | crystal population density | number/cm3/cm |
| n( | intercept of the CSD | number/cm3/cm |
| p | exponent for the growth rate vs. cooling rate relation given by Cashman (1993) | dimensionless |
| t | time | hours |
| T1 (or TS) | solidus temperature | 900 (C |
| T2 (or TL) | liquidus temperature | 1140 (C |
| x’ | distance from the sill/wallrock contact within the sill | meters |
| 1 | thermal diffusivity of country rock and solidified magma | 5.470 x 10-3 m2/hour |
| 2 | thermal diffusivity of the magma | 2.218 x 10-3 m2/hour |
|  | root of eq. (3) of Jaeger (1957): | 3.131 x 10-1, dimensionless |